| Feature | English / Metric |
| --- | --- |
| Brush Drive System |
| Brush bristle length | 0.87-inch/ 22 mm |
| Brush bristle type | Nylon construction, reverse chevron |
| Brush diameter | 3.5-inch/ 89 mm |
| Brush length | 15-inch/ 380 mm |
| Brush motor power | .4 hp / 298 watts |
| Brush motor voltage | 120 V / 230 V |
| Brush RPM | 1,200 rpm |
| Motor RPM | 2,400 rpm |
| Chassis/Body Construction |
| Chassis construction | Cast aluminum frame, rotational molded tanks and injection molded plastic cover |
| Metal parts coating | Clear Zinc |
| Wheel descriptions (non-marring) | 8” / 200 mm |
| Vacuum System |
| Airflow at orifice | 99 ft³/min / 2.8 m³/min |
| Vacuum motor amps | 7.1 amps/ 3.6 amps |
| Vacuum motor power | 1.2 hp/ 880 watts |
| Vacuum motor stages | 2 stage |
| Sealed waterlift | 86-inch/ 2184 mm |
| Machine Dimensions (Handle folded flat for storage) |
| Length | 26.8-inch / 680 mm |
| Machine Width | 19.3-inch / 490 mm |
| Height | 27.9-inch / 709 mm |
| Weight | 102 lb / 46.3 kg |
| Solution & Recovery System |
| Solution tank capacity | 5 gallon/ 19 liter |
| Recovery tank wet capacity | 5 gallon/ 19 liter |
| Spray jet count | 2-quick disconnect |
| Power Consumption |
| Amps | 10.8 amps/ 5.4 amps |
| Voltage | 120 V / 230 V |
| Watts | 1300 watts |
| Cord | 50 ft / 15.2 m |
| Pump System |
| Solution pump pressure | 65 psi/ 45.36 kPa |
| Solution pump amps | .7 amp / .35 amp |
| Solution pump flow rate | .7 gpm / 2.65L |
| Sound Level |
| Decibel rating @ operators ear | 69 dBa |
| Warranty | 24 months (or max. 2000 hrs running hours) on parts and 12 months (or max.1000hr running hours) on labor, whichever comes first, excluding wear items. |

# Text boxes

### Model E5 Specifications

# SELF-CONTAINED CARPET EXTRACTOR